Drumkid quick start guide

1) Insert batteries - unscrew the 6 thumbscrews on the back of Drumkid (you don't need a screwdriver), remove the back plate, and insert 3 AA batteries (rechargeable or regular). Alternatively, connect a USB mini cable to power the device. Carefully re-tighten the thumbscrews.

2) Connect audio - plug 3.5mm audio cable (mono or stereo) or a pair of headphones into the audio output.

3) Turn on and test - slide the power switch (top right on the front panel) from "0" to "1". The lights should flash briefly in a random pattern. Now press the "start/stop" button. The lights should flash in time to a drum beat, which you should be able to hear through the headphones.

4) Get to know the controls - try turning the "chance" control (the knob on the left) and the “midpoint” control (on the right). As long as “midpoint” is set high enough, you should hear more random drum hits as the “chance” parameter increases. Now try adjusting “zoom” and “range” to see what they do.

5) Try other parameters/effects - press the "B" button to switch to the second group of parameters. The knobs will now perform different functions. Try the left knob again - it will now change the pitch of the samples or make them play in reverse.

6) Randomise all the parameters - try pressing the A, B and D buttons simultaneously to generate a new random beat. Use these as a starting point to explore the different parameters.

7) Read the full manual online at mattbradshawdesign.com for detailed information about the different parameters, MIDI control, saving/loading sessions, troubleshooting, hacking Drumkid, etc.

If you have any problems, feel free to email me at
matthewloydbradshaw@gmail.com